Moen Incorporated	October 2008

25300 Al Moen Drive

North Olmsted, Ohio  44070

Toll Free	(800) 289-6636

Website	www.moencommercial.com

E-mail	specmoen@moen.com

Product Guide Specification

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition.

This section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.

Section numbers and titles are from MasterFormat 1995 Edition, with section numbers and titles from MasterFormat 2004 Edition in parentheses.  Delete version not required.

SECTION 15410 (22 42 16)

COMMERCIAL SINKS

Specifier Notes:  This section covers Moen Commercial Model 22122 double-bowl kitchen sink.  Consult Moen Commercial for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Double-bowl kitchen sinks.

1.2	RELATED REQUIREMENTS

Specifier Notes:  Edit the following list of related sections as required.  Delete related sections not required.  List other sections with work directly related to this section.

A.	Section 15140 (22 11 00) – Domestic Water Piping (Facility Water Distribution):  Supply connections to commercial plumbing fixtures.

B.	Section 15150 (22 13 00) – Sanitary Waste and Vent Piping (Facility Sanitary Sewerage):  Waste connections to commercial plumbing fixtures.

C.	Section 15410 (22 42 39) – Commercial Faucets.

1.3	REFERENCE STANDARDS

Specifier Notes:  List reference standards mentioned in this section, complete with designations and titles.  Delete reference standards not included in this edited section.  This article does not require compliance with reference standards, but is merely a listing of those used.

A.	ASME A112.19.3 – Stainless Steel Plumbing Fixtures (Designed for Residential Use).

1.4	SUBMITTALS

Specifier Notes:  Edit submittal requirements as required.  Delete submittals not required.

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer’s product data, including installation instructions.

Specifier Notes:  Delete samples if not required.

C.	Samples:  Submit manufacturer’s samples for selection of finish.

D.	Manufacturer’s Certification:  Submit manufacturer’s certification that materials comply with specified requirements and are suitable for intended application.

E.	Cleaning Instructions:  Submit manufacturer’s cleaning instructions.

F.	Warranty Documentation:  Submit manufacturer’s standard warranty.

1.5	QUALITY ASSURANCE

A.	Manufacturer’s Qualifications:  Manufacturer regularly engaged for past 10 years in manufacture of commercial sinks of similar type to that specified.

1.6	DELIVERY, STORAGE, AND HANDLING

A.	Delivery and Acceptance Requirements:  Deliver materials to site in manufacturer’s original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage and Handling Requirements:

1.	Store and handle materials in accordance with manufacturer’s instructions.

2.	Keep materials in manufacturer’s original, unopened containers and packaging until installation.

3.	Store materials in clean, dry area indoors.

4.	Protect materials and finish during storage, handling, and installation to prevent damage.

1.7	WARRANTY

A.	Warranty Period:  5 years.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	Moen Incorporated, 25300 Al Moen Drive, North Olmsted, Ohio 44070.  Toll Free (800) 289-6636.  Website www.moencommercial.com.  E-mail specmoen@moen.com.

2.2	COMMERCIAL SINKS

A.	Double-Bowl Kitchen Sinks:  Model 22122.

1.	Material:  18-gauge, Type 301 stainless steel.

2.	Bowl Dimensions:

a.	Left:  14 inches by 16 inches by 7 inches deep.

b.	Right:  14 inches by 16 inches by 11 inches deep.

3.	Sink Ledge:  Four fixture-mounting holes, 1-1/2-inch diameter, 4 inches on center.

4.	Recessed Drain Openings:  Two 3-1/2-inch diameter.

5.	Undercoating:  Fully undercoated with sound and temperature insulating material, including sound pads.

6.	Finish:  Exposed surfaces polished to lustrous satin-tone finish.

7.	Mounting:  Continuous U-channel and sink clamps.

8.	Cut-Out Dimensions:

a.	32-3/8 inches by 21-3/8 inches.

b.	Corner Radius:  1-1/4 inches.

c.	Tolerance:  Plus or minus 1/16 inch.

9.	Compliance:  ASME A112.19.3.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine countertops to receive double-bowl kitchen sinks.

B.	Notify Architect of conditions that would adversely affect installation or subsequent use.

C.	Do not begin installation until unacceptable conditions are corrected.

3.2	INSTALLATION

A.	Install double-bowl kitchen sinks in accordance with manufacturer’s instructions at locations indicated on the Drawings.

B.	Install double-bowl kitchen sinks level, plumb, and secure in countertops.

C.	Apply joint sealant to countertops in accordance with manufacturer’s instructions.

3.3	CLEANING

A.	Clean double-bowl kitchen sinks promptly after installation in accordance with manufacturer’s instructions.

B.	Do not use harsh cleaning materials or methods that could damage finish.

3.4	PROTECTION

A.	Protect installed double-bowl kitchen sinks from damage during construction.

B.	Do not permit use of double-bowl kitchen sinks before final acceptance.

END OF SECTION