Moen Incorporated	August 2010

25300 Al Moen Drive

North Olmsted, Ohio  44070

Toll Free	(800) 289-6636

Website	www.moencommercial.com

E-mail	specmoen@moen.com

Product Guide Specification

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition.

This section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.

Section numbers and titles are from MasterFormat 1995 Edition, with section numbers and titles from MasterFormat 2004 Edition in parentheses.  Delete version not required.

SECTION 15410 (22 42 39)

COMMERCIAL HAND-HELD SHOWER SYSTEMS

Specifier Notes:  This section covers Moen Commercial Model 52710 hand-held shower system.  Consult Moen Commercial for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Hand-held shower systems.

1.2	RELATED REQUIREMENTS

Specifier Notes:  Edit the following list of related sections as required.  Delete related sections not required.  List other sections with work directly related to this section.

A.	Section 15140 (22 11 00) – Domestic Water Piping (Facility Water Distribution):  Supply connections to commercial plumbing fixtures.

B.	Section 15150 (22 13 00) – Sanitary Waste and Vent Piping (Facility Sanitary Sewerage):  Waste connections to commercial plumbing fixtures.

1.3	REFERENCE STANDARDS

Specifier Notes:  List reference standards mentioned in this section, complete with designations and titles.  Delete reference standards not included in this edited section.  This article does not require compliance with reference standards, but is merely a listing of those used.

A.	ANSI/ASSE 1014 – Performance Requirements for Backflow Prevention Devices for Hand-Held Showers.

- ASME A112.18.1/CSA B125.1 – Plumbing Supply Fittings.

- ASSE 1016 – Automatic Compensating Valves for Individual Showers and Tub/Shower   
   Combinations.

D.	ADA – Americans with Disabilities Act

1.4	SUBMITTALS

Specifier Notes:  Edit submittal requirements as required.  Delete submittals not required.

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer’s product data, including installation instructions.

Specifier Notes:  Delete samples if not required.

C.	Samples:  Submit manufacturer’s samples for selection of finish.

D.	Manufacturer’s Certification:  Submit manufacturer’s certification that materials comply with specified requirements and are suitable for intended application.

E.	Operation and Maintenance Instructions:  Submit manufacturer’s operation and maintenance instructions, including cleaning instructions and parts list.

F.	Warranty Documentation:  Submit manufacturer’s standard warranty.

1.5	QUALITY ASSURANCE

A.	Manufacturer’s Qualifications:  Manufacturer regularly engaged for past 10 years in manufacture of commercial plumbing fixtures of similar type to that specified.

1.6	DELIVERY, STORAGE, AND HANDLING

A.	Delivery and Acceptance Requirements:  Deliver materials to site in manufacturer’s original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage and Handling Requirements:

1.	Store and handle materials in accordance with manufacturer’s instructions.

2.	Keep materials in manufacturer’s original, unopened containers and packaging until installation.

3.	Store materials in clean, dry area indoors.

4.	Protect materials and finish during storage, handling, and installation to prevent damage.

1.7	WARRANTY

A.	Warranty Period:  5 years.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	Moen Incorporated, 25300 Al Moen Drive, North Olmsted, Ohio 44070.  Toll Free (800) 289-6636.  Website www.moencommercial.com.  E-mail specmoen@moen.com.

2.2	COMMERCIAL HAND-HELD SHOWER SYSTEMS

Specifier Notes:  Refer to Moen Commercial Products Catalog for tub/shower accessories.

A.	Hand-Held Shower Systems:  Model 52710LF16.

1.	Hand-Held Shower:

a.	Spray-Wand Height:  9-1/2 inches.

b.	Spray-Head Diameter:  3-3/16 inches.

2.	Hose:  69-inch metal double-swivel hose assembly.

3.	Slide Bar:  30-inch metal slide bar with hardware.  Not for use as grab bar.

4.	Chrome-Plated Metal:

a.	Drop ell.

b.	Vacuum breaker.

5.	Flow:  Maximum 1.6 gpm (6.0 L/min) at 60 psi.

6.	Compliance:

a.	ASSE 1014

b.      ASME A112.18.1/CSA B125.1

c.      ASSE 1016

d.      ADA

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive hand-held shower systems.

B.	Notify Architect of conditions that would adversely affect installation or subsequent use.

C.	Do not begin installation until unacceptable conditions are corrected.

3.2	INSTALLATION

A.	Install hand-held shower systems in accordance with manufacturer’s instructions at locations indicated on the Drawings.

B.	Install hand-held shower systems level, plumb, without leaks, and secure to wall.

3.3	ADJUSTING

A.	Adjust hand-held shower systems for proper operation in accordance with manufacturer’s instructions.

B.	Remove and replace damaged components that cannot be successfully repaired.

3.4	CLEANING

A.	Clean hand-held shower systems promptly after installation in accordance with manufacturer’s instructions.

B.	Do not use harsh cleaning materials or methods that could damage finish.

3.5	PROTECTION

A.	Protect installed hand-held shower systems from damage during construction.

B.	Do not permit use of hand-held shower systems before final acceptance.

END OF SECTION