Moen Incorporated	July 2008

25300 Al Moen Drive

North Olmsted, Ohio  44070

Toll Free	(800) 289-6636

Website	www.moencommercial.com

E-mail	specmoen@moen.com

Product Guide Specification

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition.

This section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.

Section numbers are from MasterFormat 1995 Edition, with section numbers from MasterFormat 2004 Edition in parentheses.  Delete version not required.

SECTION 10810 (10 28 13.13)

COMMERCIAL HOSE BRACKETS

Specifier Notes:  This section covers Moen Commercial Model 8199 hose bracket with rubber hose.  Consult Moen Commercial for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Hose brackets with rubber hose.

1.2	SUBMITTALS

Specifier Notes:  Edit submittal requirements as required.  Delete submittals not required.

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer’s product data, including installation instructions.

1.3	DELIVERY, STORAGE, AND HANDLING

A.	Delivery and Acceptance Requirements:  Deliver materials to site in manufacturer’s original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage and Handling Requirements:

1.	Store and handle materials in accordance with manufacturer’s instructions.

2.	Keep materials in manufacturer’s original, unopened containers and packaging until installation.

3.	Store materials in clean, dry area indoors.

4.	Protect materials and finish during storage, handling, and installation to prevent damage.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	Moen Incorporated, 25300 Al Moen Drive, North Olmsted, Ohio 44070.  Toll Free (800) 289-6636.  Website www.moencommercial.com.  E-mail specmoen@moen.com.

2.2	COMMERCIAL HOSE BRACKETS

A.	Hose Brackets with Rubber Hose:  Model 8199.

1.	Hose Bracket:

a.	Stainless steel.

b.	Anti-slip spring-loaded handle grip with stainless steel screws.

2.	Rubber Hose:  36-inch heavy-duty hose with female garden hose threaded connection.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive hose brackets with rubber hose.

B.	Notify Architect of conditions that would adversely affect installation or subsequent use.

C.	Do not begin installation until unacceptable conditions are corrected.

3.2	INSTALLATION

A.	Install hose brackets with rubber hose in accordance with manufacturer’s instructions at locations indicated on the Drawings.

B.	Install hose brackets with rubber hose level and secure to wall.

3.3	PROTECTION

A.	Protect installed hose brackets with rubber hose from damage during construction.

END OF SECTION